## Slide 1: Chapter 14
Applications of UV-VIS(160-780 nm)
Molecular Absorption Spectrometry

## Slide 2: UV-VIS Studies in General
Quantitative UV-VIS studies are quite numerous and widespread
  basic chemical research
  regular clinical studies
  industrial streams
  wastewater streams
  forensics
  etc etc etc

## Slide 3: UV-VIS Studies: 
values range from 0  105
= 8.7 x 1019 P·A
P = transition probability
QM-allowed transitions, P ~ 0.1-1
A = cross section target area
(typical organic molecule, A ~ 10-15 cm2)
e.g.,  = 8.7 x 1019 (0.89) (10-15 cm2)
 = 7.7 x 104 L/cm·mol
Strong absorption bands, max ~ 104-105
Low intensity bands, max < 103
QM-forbidden transitions, P < 0.01

## Slide 4: Absorption - Relaxation
Absorption process:
M + hn  M*  (?)
(t1/2 ~ 10-8 – 10-9 sec)
Relaxation processes:
M*  M + heat (most common)
M*  A + B (photochemical RXN)
M*  M + hn (fluorescence, phosphorescence)

## Slide 5: Foundations of Absorption Studies
Absorption usually correlated with excitation of bonding electrons
 λ location associatied with bond types
 functional groups
(good for identification purposes)
 quantitative evaluation
(via Beer-Lambert Law, A = ·b·c)

## Slide 6: “Visible” Spectra: Micro-environmental Effects
Fig. 14-1, pg 368 Visible absorption spectra for 1,2,4,5-tetrazine
(a) gas phase,
(b) in nonpolar solvent,
(c) in polar solvent.

## Slide 7: Types of Transitions in UV-VIS
Three types of transitions
1. p, s, and n electrons
(organics, molecular/ionic + inorganics)
2. d & f electrons
(transition metal complexes)
3. charge transfer electrons

## Slide 8: Types of Transitions
Electron distribution in  and  molecular orbitals.

## Slide 9: Types of Transitions
Types of molecular orbitals in formaldehyde.

## Slide 10: Absorbing Species Containing p, s, and n Electrons
Electronic molecular energy levels.
n
p*
p
s
s*
s*
Antibonding
Antibonding
Nonbonding
Bonding
Bonding
p
p*
n
p*
n
s*
s

## Slide 11: Types of Transitions
σ  σ* vacuum UV (λ < 185 nm)
n  σ* normally below 200 nm
  low ε (100  3000)
n, π  π* 200-700 nm
low ε n  π* (10  100)
low ε π  π* (1000  15000)
for organics, requires presence of unsaturated chromophores
Spectra usually quite complex due to overlapping vibrational and rotational transitions……broadband absorption results rendering QM treatment qualitative at best

## Slide 12: Types of Transitions

## Slide 13: UV Spectra
Fig. 14-2. Absorption spectra for typical organic compounds.

## Slide 14: Types of Transitions

## Slide 15: Types of Transitions in UV-VIS
Three types of transitions
1. p, s, and n electrons
2. d & f electrons
3. charge transfer electrons

## Slide 16: Absorption by Elements of the First and Second Transition Series
These all involve 3d electrons

## Slide 17: Absorption by Elements of the First and Second Transition Series
Ligand Field Theory
"Absorption spectra of some transition-metal ions."

## Slide 18: Absorption by Elements of the First and Second Transition Series
Ligand Field Theory
"Electron-density distribution in the five d-orbitals."

## Slide 19: Absorption by Elements of the First and Second Transition Series
Ligand Field Theory
"Effect of ligand field on d-orbital energies."

## Slide 20: Absorption by Elements of the First and Second Transition Series
Ligand Field Theory
"Effect of Ligands on Absorption Maxima Associated with
d  d transitions."

## Slide 22: Absorption by Lanthanides/Actinides
These involve 4f and 5f electrons

## Slide 23: Absorption by d & f electrons
Transitions between filled and unfilled levels Energies depend on ligand types…..recall spectrochemical series
Varies with PT position and oxidation states
4f,5f electrons more shielded by higher n electrons…leads to bands that are narrower than bands generated by 3d electrons

## Slide 24: Types of Transitions in UV-VIS
Three types of transitions
1. p, s, and n electrons
2. d & f electrons
3. charge transfer electrons

## Slide 25: Charge-Transfer Absorption
 > 10000……highly sensitive measurements
complex consists of an electron-donor group (usually a ligand) bonded to an electron acceptor (usually a metal) …provides for means of internal electron transfer (i.e., upon absorption of hν) like in REDOX processes
if complex involves a metal, the metal usually acts as the electron acceptor….some acceptions

## Slide 26: Charge-Transfer Absorption

## Slide 27: Qualitative Applications of UV-VIS

## Slide 28: Qualitative Applications of UV-VIS
"Effect of Multichromophores on Absorption."

## Slide 29: Qualitative Applications of UV-VIS
Table 14-4 "Absorption Characteristics of Aromatic Compounds."

## Slide 30: Qualitative Applications of UV-VIS

## Slide 31: Analysis of Mixtures of Absorbing Substances
Selection of Wavelength
Fig. 14-9, pg. 377 "Absorption spectrum of a two-component mixture (M+N) with spectra of the individual components. Vertical dashed lines indicate optimal wavelengths for determiniation of the two components."

## Slide 32: Analysis of Mixtures of Absorbing Substances
Solution of Binary Mixture
Schematic representation of the absorption spectra of solutions containing
(1) c1 moles per liter of substance 1
(2) c2 moles per liter of substance 2
(3) c1 moles per liter of substance 1 and
c2 moles per liter of substance 2."

## Slide 33: Solution of Binary Mixture
Wavelength 1
Am,l1 = 1,l1*b*c1 + 2,l1*b*c2
Am,l1 = (1,l1*c1 + 2,l1*c2)*b
Wavelength 2
Am,l2 = 1,l2*b*c1 + 2,l2*b*c2
Am,l2 = (1,l2*c1 + 2,l2*c2)*b

## Slide 34: Solution of Binary Mixture
let A1 = Am,l1 A2 = Am,l2
D1 = 1,l1 D2 = 1,l2
E1 = 2,l1 E2 = 2,l2
then A1 = (D1*c1 + E1*c2)*b
A2 = (D2*c1 + E2*c2)*b

## Slide 35: Solution of Binary Mixture
solve for c2
A2/b = (D2*c1 + E2*c2)
A2/b - D2*c1 = E2*c2
c2 = (A2/(b*E2) - (D2*c1)/E2

## Slide 36: Solution of Binary Mixture
then
A1 = (D1*c1 + E1((A2/(b*E2)-(D2*c1)/E2))*b
A1/b = (D1*c1 + E1((A2/(b*E2)-(D2*c1)/E2))
A1/b = (c1(D1 - D2*(E1/E2))+(E1/E2)*(A2/b))
A1/b - (A2/b)*(E1/E2) = c1(D1-D2*(E1/E2))

## Slide 37: Solution of Binary Mixture
thus
(A1/b - (A2/b)*(E1/E2))
c1 = -------------------------------
(D1 - D2*(E1/E2))
and
C2 = (A2/(E2*b) - (D2*c1)/E2

## Slide 38: Method of Standard Addition
Al cs Vs
cx = ---------------
(A2 - Al )Vx
Example 14-2 based on this……see if you can
catch the error…:o)

## Slide 39: Derivative and Dual Wavelength Spectrophotometry
Idea is to reveal spectral details only subtly present in normal A vs. λ scan
S/N degrades w/derivatization…but OK in UV-VIS
Equipment more costly
(i) microcomputer controlled
dT/dλ numerically via least-squares polynomial fitting
(ii) analog instruments
dT/dλ via use of differentiating OPAMP
(iii) λ modulation via a number of mechanical means

## Slide 40: Derivative Spectroscopy

## Slide 41: Photometric Titrations
Fig. 14-12, pg. 380 "Typical photometric titration curves. Molar absorptivities of the analyte, the product, and the titrant are given by eA, eP, eT, respectively."
Must obey Beer’s Law
Must correct A by (V+v)/V

## Slide 42: Time-Based Kinetics Studies

## Slide 43: Time-Based Kinetics Studies

## Slide 44: Photoacoustic Spectroscopy
“Block diagram of a single-beam photoacoustic spectrometer with digital data processing.”
Good for UV-VIS-IR of solids, semisolids, turbid liquids, gases
e.g., minerals, semiconductors, TLC plates, natural products, coatings on surfaces, NO in upper atmosphere

## Slide 45: Photoacoustic Spectroscopy
“Photoacoustic spectra of smears of blood and blood components.”

## Slide 46: Photoacoustic Spectroscopy
http://nte-serveur.univ-lyon1.fr/spectroscopie/photoaccoustiques/Web_PAS5.htm